## Slide 1: EE-2003 Computer Organization & Assembly Language

## Slide 2: Chapter No: 06
Conditional Processing

## Slide 3
Bit-wise Operations
Notes: Bit Masking

## Slide 4: Status Flags (Revision)
• The Zero flag is set when the result of an operation equals zero.
• The Carry flag is set when an instruction generates a result that is too large (or too small) for the destination operand.
• The Sign flag is set if the destination operand is negative, and it is clear if the destination operand is positive.
• The Overflow flag is set when an instruction generates an invalid signed result.
• The Parity flag is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
• The Auxiliary Carry flag is set when an operation produces a carry out from bit 3 to bit 4.

## Slide 5: NOT Instruction
Performs a bitwise Boolean NOT operation on a single destination operand
Syntax: (no flag affected)
NOT destination
Example:
mov al 11110000b
NOT al

## Slide 6: AND Instruction
Performs a bitwise Boolean AND operation between each pair of matching bits in two operands
AND instruction always clears Overflow and Carry flag. Also can modify Sign, Zero, and Parity in a way that is consistent with the value assigned to the destination operand.
Syntax: AND destination, source
Example:
mov al, 00111011b
and al, 00001111b

## Slide 7: OR Instruction
Performs a bitwise Boolean OR operation between each pair of matching bits in two operands
Syntax: Clears Overflow, Cary . Modifies Sign, Zero, and Parity in a way that is consistent with the value assigned to the destination operand
Syntax: OR destination, source
Example:
mov al, 00111011b
or al, 00001111b

## Slide 8: XOR Instruction
Performs a bitwise Boolean XOR operation between each pair of matching bits in two operands
The XOR instruction always clears the Overflow and Carry flags.
Syntax: XOR destination, source
Example:
mov al, 00111011b
xor al, 00001111b
XOR is a useful way to invert the bits in an operand and data encryption

## Slide 9: Applications
Convert the character in AL to upper case
Solution: Use the AND instruction to clear bit 5
mov al , 'a’ ; AL = 01100001b
and al , 11011111b ; AL = 01000001b
Convert a binary decimal byte into its equivalent ASCII decimal digit
Solution: Use the OR instruction to set bits 4 and 5
mov al , 6 ; AL = 00000110b
or al , 00110000b ; AL = 00110110b
Jump to a label if an integer is even
Solution: AND the lowest bit with a 1, If the result is Zero, the number was even
mov ax , wordVal
and ax , 1 ; low bit set?
jz EvenValue ; jump if Zero flag

## Slide 10: Applications
Jump to a label if the value in AL is not zero
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction
or al , al
jnz IsNotZero ; jump if not zero

## Slide 11
Non-Destructive Instructions
Notes: Bit Masking

## Slide 12: TEST Instruction
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified, but the flags are affected
The TEST instruction always clears the Overflow and Carry flags
Example: jump to a label if either bit 0 or bit 1 in AL is set
test al, 00000011b
jnz ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set
test al, 00000011b
jz ValueNotFound

## Slide 13: CMP Instruction
Compares the destination operand to the source operand
  Nondestructive subtraction of source from destination (destination operand is not changed)
Syntax:
CMP destination, source
Example: destination == source
mov al , 5
cmp al , 5 ; Zero flag set
Example: destination < source
mov al , 4
cmp al , 5 ; Carry flag set
Example: destination > source
mov al , 6
cmp al , 5 ; ZF = 0, CF = 0
The comparisons shown so far were unsigned

## Slide 14: CMP Instruction
The comparisons shown here are performed with signed integers
Example: destination > source
mov al , 5
cmp al , -2 ; Sign flag == Overflow flag
Example: destination < source
mov al , -1
cmp al , 5 ; Sign flag != Overflow flag

## Slide 15: Conditions and Output
Unsigned | ZF | CF
destination < source | 0 | 1
destination > source | 0 | 0
destination = source | 1 | 0
Signed | FLAGS
destination < source | SF != OF
destination > source | SF == OF
destination = source | ZF = 1

## Slide 16: Setting and Clearing Individual Flags
and al , 0 ; set Zero
or al , 1 ; clear Zero
or al , 80h ; set Sign
and al , 7Fh ; clear Sign
stc ; set Carry
clc ; clear Carry
mov al , 7Fh
inc al ; set Overflow
or eax , 0 ; clear Overflow

## Slide 17: BT (Bit Test) Instruction
Copies bit from an operand into the Carry flag
Syntax:
BT reg/mem16 , reg16/reg32/imm
BT reg/mem32 , reg16/reg32/imm
Example: jump to label L1 if bit 9 is set in the AX register
bt AX , 9 ; CF = bit 9
jc L1 ; jump if Carry
There are three more BT instructions:
  BTC bitBase, n ; bit test and complement
  BTR bitBase, n ; bit test and reset (clear)
  BTS bitBase, n ; bit test and set

## Slide 18
Conditional jumps

## Slide 19: Conditional Structures
There are no high-level logic structures such as if-then-else, in the IA-32 instruction set
  But, you can use combinations of comparisons and jumps to implement any logic structure
First, an operation such as CMP, AND or SUB is executed to modified the CPU flags
Second, a conditional jump instruction tests the flags and changes the execution flow accordingly
Example:
cmp eax,0 and dl,10110000b
jz L1 ; jump if ZF = 1 jnz L2 ; jump if ZF = 0
. . ….
L1: L2:

## Slide 20: Jcond Instructions
A conditional jump instruction branches to a label when specific register or flag conditions are met
Jcond Destination
Four groups: (some are the same)
  based on specific flag values
  based on equality between operands
  based on comparisons of unsigned operands
  based on comparisons of signed operands

## Slide 21: Jumps Based on Specific Flags
Flag | Instruction | Description | Flag Status
ZERO | JZ | Jump if zero | ZF = 1
 | JNZ | Jump if not zero | ZF = 0
CARRY | JC | Jump if carry | CF = 1
 | JNC | Jump if not carry | CF = 0
Over-Flow | JO | Jump if overflow | OF = 1
 | JNO | Jump if not overflow | OF = 0
SIGN | JS | Jump if sign | SF = 1
 | JNS | Jump if not sign | SF = 0
PARITY | JP | Jump if parity (even) | PF = 1
 | JNP | Jump if not parity (odd) | PF = 0

## Slide 22: Jumps Based on Equality
Instruction | Description
JE | Jump if equal (left OP = right OP)
JNE | Jump if not equal (left OP right OP)
JCXZ | Jump if CX = 0
JECXZ | Jump if ECX = 0
Instruction | Description
JE | Jump if equal (left OP = right OP)
JNE | 
JCXZ | Jump if CX = 0
JECXZ | Jump if ECX = 0

## Slide 23: Jumps Based on Un-signed Comparison
Condition | Instruction | Description
 | JA | Jump if above
 | JNA | Jump if not above
 | JAE | Jump if above and equal
 | JNAE | Jump if not above and equal
 | JB | Jump if below
 | JNB | Jump if not below
 | JBE | Jump if below and equal
 | JNBE | Jump if not below and equal
Condition | Instruction | Description
 | JA | 
 | JNA | 
 | JAE | 
 | JNAE | 
 | JB | 
 | JNB | 
 | JBE | 
 | JNBE | 

## Slide 24: Jumps Based on Signed Comparison
Condition | Instruction | Description
 | JG | Jump if greater
 | JNG | Jump if not greater
 | JGE | Jump if greater and equal
 | JNGE | Jump if not greater and equal
 | JL | Jump if less than
 | JNL | Jump if not less than
 | JLE | Jump if less than and equal
 | JNLE | Jump if not less than and equal
Condition | Instruction | Description
 | JG | 
 | JNG | 
 | JGE | 
 | JNGE | 
 | JL | 
 | JNL | 
 | JLE | 
 | JNLE | 

## Slide 25: EXAMPLES

## Slide 26: EXAMPLES (Signed CMP)

## Slide 27: Examples
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large
Solution:
  mov Large , bx
  cmp ax , bx
  jna Next
  mov Large , ax
Next:
Compare signed AX to BX, and copy the smaller of the two into a variable named small
Solution:
  mov small , ax
  cmp bx , ax
  jnl Next
  mov small , bx
Next:

## Slide 28: Examples
Find the first even number in an array of unsigned Integers
Solution:
.date
intArray DWORD 7, 9, 3, 4, 6, 1
.code
...
mov ebx, OFFSET intArray
mov ecx, LENGTHOF intArray
L1: test DWORD PTR [ebx], 1
jz found
add ebx, 4
loop L1
...
Found:

## Slide 29
Conditional Structures

## Slide 30: If Statements
If then else
JNE esle
JMP endif
else:
endif:
Condition
Then
Else
Condition
Then
Else

## Slide 31: Block-structured If Statements
Assembly language programmers can easily translate logical statements written in C++ into assembly language. For example
if( op1 == op2 )
X = 1;
else
X = 2;
JNE else
JMP endif
else:
Endif:
Condition
Then
Else
JNE else
JMP endif
else:
Endif:
Mov EAX, op1
CMP EAX, op2
MOV X , 1
MOV X , 2

## Slide 32: Exercise
Implement the following pseudocode in assembly language, all values are unsigned:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
JA endif
Endif:
CMP EBX, ECX
MOV EAX , 5
MOV EDX , 6

## Slide 33: Exercise
Implement the following pseudocode in assembly language, all values are 32-bit signed integer
if( va1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
JG else
JMP endif
else:
Endif:
Mov EAX, var1
CMP EAX, var2
MOV var3 , 10
MOV var3 , 6
MOV var4 , 7
JLE if
JMP endif
if:
Endif:
Mov EAX, var1
CMP EAX, var2
MOV var3 , 10
MOV var3 , 6
MOV var4 , 7

## Slide 34: Compound Expression with AND
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped
if(al > bl && bl > cl)
X = 1;
cmp al,bl ;1st expression
ja L1
jmp next
L1:
cmp bl,cl ;2nd expression
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:
cmp al,bl ;1st expression
jbe next
cmp bl,cl ;2nd expression
jbe next
mov X,1 ; set X to 1
next:

## Slide 35: Compound Expression with OR
In the following example, if the first expression is true, the second expression is skipped
if(al > bl || bl > cl)
X = 1;
cmp al,bl ;1st expression
jbe L1
jmp L2
L1:
cmp bl,cl ;2nd expression
jbe next
L2: ; both are true
mov X,1 ; set X to 1
next:
cmp al,bl ;1st expression
ja L1
cmp bl,cl ;2nd expression
jbe next
L1:
mov X,1 ; set X to 1
next:

## Slide 36: Exercise
Implement the following pseudocode in assembly language, all values are unsigned:
if( ebx <= ecx && ecx > edx)
{
eax = 5;
edx = 6;
}
Endif:
CMP EBX, ECX
JA endif
CMP ECX, EDX
JBE endif
MOV EAX , 5
MOV EDX , 6

## Slide 37: While Loop
A WHILE loop is really an IF statement followed by the body of the loop followed by an unconditional jump to the top of the loop
Consider the following example
while( eax < ebx)
eax = eax + 1;
_While:
Jmp _while
_endwhile:
CMP EAX, EBX
JAE _endwhile
Inc EAX

## Slide 38: Exercise
Implement the following loop, using unsigned 32-bit integer
while( ebx <= val1)
{
eax++;
if (ebx == ecx)
X=2;
else
X=3;
}
_While:
Jmp _while
_endwhile:
CMP EBX, val1
JA _endwhile
INC EAX
CMP EBX, ECX
JNE else
MOV X, 2
Jmp _while
else:
MOV X, 3

## Slide 39: Do Loop
A DO loop is really an IF statement, here the body of the loop followed by an IF statement to unconditional jump
Consider the following example
Do
{
eax = eax + 1;
}while( eax < ebx)
_do:
Jmp _do
_enddo:
CMP EAX, EBX
JAE _enddo
Inc EAX

## Slide 40: LOOPZ and LOOPE Instruction
Syntax:
  LOOPE destination
  LOOPZ destination
Logic:
  ECX ← ECX – 1
  if ECX != 0 and ZF=1, jump to destination
The destination label must be between -128 and +127 bytes from the location of the
following instruction
Useful when scanning an array for the first element that meets some condition

## Slide 41: LOOPNZ and LOOPNE Instruction
Syntax:
  LOOPNE destination
  LOOPNZ destination
Logic:
  ECX ← ECX – 1
  if ECX != 0 and ZF=0, jump to destination
The destination label must be between -128 and +127 bytes from the location of the
following instruction
Useful when scanning an array for the first element that meets some condition

## Slide 42: Examples
The following code finds the first positive value in an array:
Solution:
.data
array SWORD -3,-6,-1,-10,10,30,40,4
sentinel SWORD 0
.code
mov esi , OFFSET array
mov ecx , LENGTHOF array
next:
test WORD PTR [esi] , 8000h ; test sign bit
pushfd ; push flags on stack
add esi , TYPE array
popfd ; pop flags from stack
loopnz next ; continue loop
jnz quit ; none found
sub esi,TYPE array ; ESI points to value
quit:

## Slide 43: Examples
Locate the first nonzero value in the array. If none is found, let ESI point to the sentinel value
Solution:
.data
array SWORD 50 DUP (?)
sentinel SWORD 0
.code
mov esi , OFFSET array
mov ecx , LENGTHOF array
next:
cmp WORD PTR [esi] , 0 ; check for zero
pushfd ; push flags on stack
add esi , TYPE array
popfd ; pop flags from stack
loopz next ; continue loop
jz quit ; none found
sub esi,TYPE array ; ESI points to value
quit: