## Slide 1: Asynchronous Counters

## Slide 2: Lecture Overview
Classifications of Counters
Definitions
Asynchronous Counter…
  J – K Flip Flops
  D Flip Flops
  Up Counters
  Down Counters
  Truncated Counters
Design Example

## Slide 3: Classifications of Counters
Asynchronous Counters
  Only the first flip-flop is clocked by an external clock. All subsequent flip-flops are clocked by the output of the preceding flip-flop.
  Asynchronous counters are slower than synchronous counters because of the delay in the transmission of the pulses from flip-flop to flip-flop.
  Asynchronous counters are also called ripple-counters because of the way the clock pulse ripples it way through the flip-flops.

## Slide 4: Classifications of Counters
Synchronous Counters
  All flip-flops are clocked simultaneously by an external clock.
  Synchronous counters are faster than asynchronous counters because of the simultaneous clocking.
  Synchronous counters are an example of state machine design because they have a set of states and a set of transition rules for moving between those states after each clocked event.

## Slide 5: States / Modulus / Flip-Flops
The number of flip-flops determines the count limit or number of states.
    (STATES = 2 # of flip flops)
The number of states used is called the MODULUS.
For example, a Modulus-12 counter would count from 0 (0000) to 11 (1011) and requires four flip-flops (16 states - 12 used).

## Slide 9
2-Bit Asynchronous Counter using JK flip flop

## Slide 14: Asynchronous Counter Design Steps
Select Type
    Up or Down
    Modules
Select Flip-Flop Type
    J-K or D
    Positive Edge Trigger (PET) or Negative Edge Trigger (NET)
Determine Number of Flip-Flops
    (2# Flip-Flop  Modules)

## Slide 15: Asynchronous Counter Design Steps
Design Basic Counters
    Same polarity for down counters:
    Opposite polarity for up counters:
Design Limits Logic
    Input to logic is count that is one past the end of sequence.

## Slide 16: Design Example
Select Type
    Up or Down
    Modules
Select Flip-Flop Type
    J-K or D
    Positive Edge Trigger (PET) or Negative Edge Trigger (NET)
Determine Number of Flip-Flops
    (2# Flip-Flop  Modules)
MOD – 14 (0..13)
24 Flip-Flop  16

## Slide 17: Design Example
Design Basic Counters
    Same polarity for down counters:
    Opposite polarity for up counters:
Design Limits Logic
    Input to logic is count that is one past the end of sequence.
Limit 13+1 = 14 (1110)

## Slide 18: Design Example…Solution

## Slide 19
Counter Decoding

## Slide 25
Asynchronous Up/Down Counter